## Slide 1
Start PyQTM.py from Spyder

## Slide 2
This is the main panel
Experimental Data needed here

## Slide 3
This is the main panel
Experimental Data needed here
- Edit numbers into the fields (input verification with RETURN) - Make an overtone active by checking the box

## Slide 4
This is the main panel
Experimental Data needed here
Edit numbers into the fields (input verification with RETURN) - Make an overtone active by checking the box
or
- Import from Clipboard, (format shown here) - Mark range,
- CtrlC - „Point from Clbbd“

## Slide 5
Shifts are always relative to a reference state (which corresponds to the baseline in the experimental data)
These are the model parameters
These are the
experimental data

## Slide 6
This is the reference state (no film, bulk density: 1 g/cm3, viscosity: 0.89 mPa s)

## Slide 7
Play around with the system parameters to bring the model closer to the data (thickness was chosen as 3 nm, here)

## Slide 8
Make sure to have the fit parameters activated
Click Fit Point

## Slide 9
Fitted values are here

## Slide 10
Save your work

## Slide 11
When importing a time series,
make sure to have chosen the correct format
PyQTM can do
preaveraging (if you wish)

## Slide 12
Choose a file

## Slide 13
The Clausthal group typically discards data from the fundamental
uncheck
This is what an
adsorption experiment might
look like

## Slide 14
looks better

## Slide 15
Choose the correct f_cen
Hide a range (if you wish)

## Slide 16
looks better

## Slide 17
Click „Average“ and choose the range
Click „Set Baseline“ to make this the new zero

## Slide 18
Now choose one data point as the basis for modeling
by clicking onto it
The light blue bar indicates which data point is active for fitting

## Slide 19
Make sure to have the parameters activated
Click „Fit Point“ (in case the fit was not done automatically)

## Slide 20
fitted curves
fitted parameters

## Slide 21
Export fitted values and simulation data

## Slide 22
Fitted parameters are written into the file Individual_Fits_Log
fitted curves
fitted parameters

## Slide 23
Fitted parameters are written into the file Individual_Fits_Log
fitted curves
fitted parameters

## Slide 24
To fit an entire time series, click „Select Fit Range“ and drag over the graph

## Slide 25
Fit range is indicated with bars
Click „Fit Series“

## Slide 26
Ideally, you are done (don‘t forget to save)